## Slide 1: Trinocular: Understanding Internet Reliability Through Adaptive Probing
Lin Quan, John Heidemann, Yuri Pradkin
USC/Information Sciences Institute

## Slide 2: Why Study Internet Outages?
Hurricane Sandy, Oct 2012
Japan Earthquake, Mar 2011
natural weather events and disasters
Egypt Internet shutdown, Jan 2012
Syria Internet shutdown, May 2013
political events
Home router down
link failures
network infrastructure problems

## Slide 3: Our Goal: Track All Outages, for All Internet, All The Time
Hurricane Sandy, Oct 2012
Japan Earthquake, Mar 2011
natural weather events and disasters
Egypt Internet shutdown, Jan 2012
Syria Internet shutdown, May 2013
political events
Home router down
link failures
network infrastructure problems
3.4M ping-responsive IPv4 /24 blocks

## Slide 4: Why Study Internet Reliability?
Internet Users
  am I getting the reliability I pay for?
  which ISP is most reliable?
Network Operators
  is my ISP more reliable?
Researchers
  is Internet health improving?
  do correlated events that affect multiple ISPs?

## Slide 5: How Is Our Goal Different?
Our goal: track all Internet outages
  all ping-responsive IPv4 /24 blocks
  all the time
  with known precision
Prior work is less complete or less precise
  focus on BGP prefixes ([Hubble, NSDI’08], [iPlane, OSDI’06], etc.)
  or on-demand study of small sample ([Thunderping, IMC’11])
  or based primarily on passive analysis ([Dainotti et al., IMC’11])

## Slide 6: Why Is Outage Detection Hard?
challenges
CPU constraints on prober
  14.5M allocated /24 blocks
    5.6M reply to pings
  CPU tops @ 30k probes/s per core
Traffic on target blocks
  benchmark: “background radiation” (Wustrow, IMC ‘10): 2-3.3k probes/hour to each /24
  we want to be innocuous: us <1% of background radiation
prober ISP goodwill
  traffic => complaints
  must moderate complaints
goals
precision
  must probe frequently
accuracy
  must probe many addresses per block
full coverage
  must probe many blocks

## Slide 7: Trinocular
Trinocular: active ping probes to study reliability in Internet edge
  principled: probe only when needed (informed by Bayesian inference)
    model who will reply, and how likely
  precise: outage duration ±330s (half of probing interval)
  parsimonious: only +0.7% background radiation (at target /24, per Trinocular instance)

## Slide 8: Trinocular
Trinocular: active ping probes to study reliability in Internet edge
  principled: probe only when needed (informed by Bayesian inference)
    model who will reply, and how likely
  precise: outage duration ±330s (half of probing interval)
  parsimonious: only +0.7% background radiation (at target /24, per Trinocular instance)
  principled: probe only when needed (informed by Bayesian inference)
    model who will reply, and how likely

## Slide 9: Pings Tell You Something
positive:
block is up
negative:
block is down
But Not Everything
or
computer crashed
laptop suspended
computer address reassigned
probe or reply lost
firewall enabled
negative replies are ambiguous
time

## Slide 10: Pinging Whole Blocks Tells More
a.1
a.0
a.3
a.2
time
space
Probing whole blocks resolves ambiguity
but much traffic:
draws complaints at target
expensive at prober

## Slide 11: Probe Less with Simple Model + Bayesian Inference
Probing whole block is correct but wasteful (most probes duplicate info)
Key idea: adaptive probing
  Who: use simple block model (outage-centric)
  When: guided by Bayesian Inference
  => Minimum necessary probing per block

## Slide 12: Adaptive Probing: Probe Just Enough
=> block down
positive responses => block is up
but don’t need all 4 to learn
a.1
a.0
a.3
a.2
time
space
1. instead: probe one by one
2. find one is up
3. if try is down
=> try again
=> stop early
=> stop less early
4. several fail

## Slide 13: Ever-active: who will respond
time (2 weeks)
space (0..255 addrs)
sparse
|E(b)|=39
medium
|E(b)|=141
dense
|E(b)|=234
E(b) is who will respond (derived from 3 years of censuses)
E(b) are addresses that ever respond (in plots: green at any time)

## Slide 14: Availability: how likely they respond
consistent
A(E(b))=0.992
medium
A(E(b))=0.637
intermittent
A(E(b))=0.241
A(E(b)) is how likely E(b) responds
(from 3 years of censuses; checked at runtime)
A(E(b)) is the fraction of time an E(b) address responds (plots: % time green)

## Slide 15: Bayesian Inference: Probe Just Enough to Establish Belief
Belief (B) of block state evolves over time
  after positive response
  similarly for negative response
stop probing when belief is definitive
  down if B(U)<0.1
  up if B(U)>0.9
  too many probes? declare unknown

## Slide 16: Bayesian Inference Decides: How Many Probes Are Needed
16
1 3 1 1 1 2
ground truth
(data for complete /24)
a few probes
confirm block is still up
15 probes to confirm down
15
model: every responding |E(b)|=111, active A(E(b))=0.515
this block is sparse but consistent, so only a few probes needed

## Slide 17: More Intermittent Block
17
model: every responding |E(b)|=234, active A(E(b))=0.241
this block is dense but intermittent, so sometimes need more probes
sometimes need several probes to establish confidence
2 4 3 2 15 10 2 4 3 1

## Slide 18: Trinocular’s Probing Types
  Periodic probing => guarantees freshness
  fixed interval: 11 minutes
  Adaptive probing => guarantees accuracy
  probes to resolve uncertainty of block state
  at short time scale, usually 3s apart
  Bayesian inference determines need
  Recovery probing => guarantees correctness
  special case to handle down-to-up transition
  because non-response is ambiguous in intermittent blocks
  model determines number required
Details in paper Section 4

## Slide 19: Trinocular Instances and Outage Scope
t1
t2
d1
d2
local:
t1≠>d1
t2=>d1
global:
t1≠>d2
t2≠>d2
1 Trinocular instance sees 2 outages:
t1 ≠> d1
t1 ≠> d2
2 instances distinguish local from global:
t1 ≠> d1 BUT t2 => d1 => local to t1
t1 ≠> d2 AND t2 ≠> d2 => “global”
Multiple Trinoculars can separate
local from global outages
(future work: study where and
how many instances are needed)

## Slide 20: Trinocular
Trinocular: active ping probes to study reliability in Internet edge
  principled: probe only when needed (informed by Bayesian inference)
    model who will reply, and how likely
  precise: outage duration ±330s (half of probing interval)
  parsimonious: only +0.7% background radiation (at target /24, per Trinocular instance)
  precise: outage duration ±330s (half of probing interval)
  parsimonious: only +0.7% background radiation (at target /24, per Trinocular instance)

## Slide 21: Precision and Parsimony
Validation: does Trinocular work?
  correctness: next
  precision: within ±330s, half of probing interval
  probe rate: next
Comparison: why probe /24s?
(details in paper sections 5 and 6)

## Slide 22: Precise: Detect All Outages?
Controlled outages (random duration, 1 to 36 minutes) in test block, measured from 3 different sites (2 in US, 1 in Japan).
We detect all outages longer than 11 minutes (the probing interval)

## Slide 23: Parsimonious: Probing Rate
1% of background radiation
(1% = 20-33 pkts/hour)
our mean probe rate is less than 1% of background traffic
post-facto analysis of 48 hours operation
most blocks are probed with very little traffic

## Slide 24: What Probing Granularity?
What size block should we look at?
  routable prefixes (most prior work: [Hubble, NSDI’08], [iPlane, OSDI’06], etc.)
  large regions [Dainotti et al., IMC’11]
  individual addresses [Thunderping, IMC’11]
Huge performance advantage for bigger
  418k routable prefixes vs. 3.4M analyzable /24s (8x more work!)
But what about accuracy and precision?
  [Bush et al., IMC ‘09]: reachability ≠ routable prefixes

## Slide 25: Coverage: What’s Theoretically Possible
green: what is routed black: not routed
But active probing requires targets that respond…
the IPv4 address space
(shown on hilbert curve)
0 1 2 3 4 5 6 7…
1D:
2D:
0 1 14 15
3 2 13 12
4 7 8 11
5 6 9 10
etc.

## Slide 26: Coverage: What’s Actually Possible
prefix-based
green: has a some .1 that responds
red: no .1 responding
black: not routed
/24 block-based
green: >20 address respond
red: <20 address respond
black: not routed
(stricter than Trinocular requires)
green: possible
not possible:
red : not measurable
black: not routed

## Slide 27: Coverage: What’s Actually Possible
very different number of targets (yellow dots)
approaches trade-off:
  precision: what could they see? what precision?
  accuracy: what do they see correctly?
prefix-based
/24 block-based

## Slide 28: Coverage: Granularity and Precision
measure coverage in two sizes:
routable prefixes /24 blocks
we directly cover more blocks (more yellow dots)

## Slide 29: Coverage: Granularity and Precision
measure coverage in two sizes:
routable prefixes /24 blocks
we directly cover more blocks (more yellow dots)
prefix infers many more blocks (more green area)
but is the larger coverage of prefix-based correct?

## Slide 30: Coverage: Coarser Granularity => Poorer Accuracy
truth
under-count outages
prefix-level missed 37% of outages (undercounts)
iPlane will correct with additional traceroutes
prefix-based over-counts 25% of outages:
current approaches will miss partial availability
over-count outages
=> even though prefix-based cover more blocks through inference, this coverage has poorer accuracy
prefix-based
/24 block-based

## Slide 31: Trinocular
Trinocular: active ping probes to study reliability in Internet edge
  principled: probe only when needed (informed by Bayesian inference)
    model who will reply, and how likely
  precise: outage duration ±330s (half of probing interval)
  parsimonious: only +0.7% background radiation (at target /24, per Trinocular instance)
what does Trinocular say?

## Slide 32: Observations about the Internet
local vs. global outages
notable outages: Hurricane Sandy, Egypt, Libya, Japan
Internet availability as a whole: 99.3%
(more in paper section 7)

## Slide 33: Do Different Sites See Differently?
Prior work shows different sites see different outages
  local outages: seen at one
  global outages: seen at all
  (and in between)
We compare 3 sites
  w: ISI-west (Marina del Rey)
  c: Colorado State University (Ft. Collins, Colorado)
  j: Japan (WIDE at Keio University, near Tokyo, Japan)
Merge outage observations to find overlap

## Slide 34: Local vs. Global Outages
(future work: systematically evaluate how number of vantage points affect global outage rate)
some outages affect all, estimate 15% are global
many outages are local (near one vantage point)

## Slide 35: Hurricane Sandy: why and how
Can Trinocular see large events?
  we next look at Hurricane Sandy
  paper covers Egypt, Libya, Japan, etc.
Methodology: reanalyze of existing full-probing survey data
  data not driven by Trinocular
    reuse existing frequent probing (every 2.6s) of every address
  but we apply Trinocular-style analysis
  E(b) = all addresses
Dataset: internet_address_survey_reprobing_it51j-20121217

## Slide 36: Hurricane Sandy: overall outage rate
(each red X is amount of U.S. outage for 11 minutes)
always some outages in US:
about 0.4%
after Sandy:
U.S.-level of outages tripled to about 1.2%
(compare daily median, blue line, before and after)
gradually back to baseline after about 4 days

## Slide 37: Hurricane Sandy: outages in NY/NJ
geolocation shows outage increase due from New York/New Jersey

## Slide 38: Ongoing Work
Current work assumes accurate availability
  paper detect and discards cases where low A(E(b)) would result in false outages
Work-in-progress
  estimate A(E(b)) as side-effect of outage detection (careful: they are coupled)
  Then: long-term study of global outages

## Slide 39: Conclusion
We can now measure outages
  for the whole Internet edge (continuous probes to 3.5M /24 blocks)
  with known precision
  single prober is <1% of background radiation
Data is available
  http://www.isi.edu/ant/traces/internet_outages
  come verify or extend our results